## Slide 1
Todd LeBlanc brought two GEM-2 instruments and did several tracks with them, using multiple frequencies measuring signal responses (In-Phase and Quadrature) and estimating physical properties of the subsurface (Electrical conductivity and Magnetic susceptibility)
The following slides show:
  Free-roaming tracks using instrument GEM-2 0460,
  Tracks by instrument 7047
  Grid survey behind the vault using GEM-2 0460
Note the large volumes of various types of data collected by such instruments
  2 to 6-7 frequencies collected simultaneously and continuously in space
  Due to recording accurate GPS times, the instruments can easily be used for small-scale gridding, like done in our survey
  Records show variations in soil type, some of our targets, and other anomalies (?)

## Slide 2
In-phase looks noisy

## Slide 3
Quadrature is noisy at low frequencies but responds to targets at higher frequencies (NE part of the track)

## Slide 4
Point (0,0) on this map corresponds to the GPS pedestal near vault

## Slide 5
Quadrature is noisy at low frequencies but responds to targets at higher frequencies (NE part of the track)

## Slide 6
The following slides show roaming tracks collected using instrument GEM-2 7027
These plots may be mostly useful for Todd and Ayshia (?)
  Some records seem to be all zeros, some show drift with acquisition time or different operators (?)
  I did not attempt removing the drift and gridding the track images

## Slide 11
Next, look at the grid over targets behind the vault, GEM-2 460
The instrument was set up to operate at two frequencies: 1590 Hz and 6390 Hz
Note that the target was successfully detected
  However, it might have been useful to select smaller grid spacings (e.g., 0.5 m) in the vicinity of the target

## Slide 12
High In-Phase near target (iron water-heater tank)
In-Phase response varies between lines.
Likely because of different heights of operators?

## Slide 13
Gridded version of the preceding image

## Slide 14
High Quadrature near target ?

## Slide 15
Gridded version of the preceding image

## Slide 16
High (apparent) electrical conductivity over target

## Slide 17
Gridded version of the preceding image

## Slide 18
Total electrical conductivity estimated from both measurement frequencies
Clear positive response

## Slide 19
Gridded version of the preceding image

## Slide 20
Very clear negative magnetic susceptibility anomaly measured over target

## Slide 21
Gridded version of the preceding image

## Slide 22
The following slides show line 5 of the grid from GEM-2 0460 in detail
Note the deep trough in magnetic susceptibility and strong peaks in all other quantities appearing over the target (shown by arrows)

## Slide 28
The following slides are from the records from instrument GEM-2 7027 extracted from the time-logged survey of the roughly W-E line in the southern part of the test area.
Strong detections of targets obtained at frequencies 1530, 5310, 18330, and 63030 Hz
I have no coordinates of that line, and so the results are presented as functions of station numbers.

## Slide 29
Target 5A produces strong In-Phase peaks at all frequencies
Two other targets crossed by this profile
Note that the peaks are sampled by only about 4 – 6 points for smaller targets. big target 5A, and 1-2 points .
Next time, we need try sampling the shapes of these peaks at denser spacings, and also acquire 2-D grids over them.

## Slide 30
Target produces peaks in Quadrature EM responses. Peaks vary with frequency.

## Slide 31
Similar peaks in Electric Conductivity

## Slide 32
Similar peaks in Electric Conductivity

## Slide 33
For magnetic susceptibility, the anomalies are reversed